## Slide 1: What are Raw Sockets?
A way to pass information to network protocols other than TCP or UDP (e.g. ICMP and IGMP)
A way to implement new IPv4 protocols
A way to build our own packets (be careful here)

## Slide 2: Why Would We Use Them?
Allows us to access packets sent over protocols other than TCP / UDP
Allows us to process IPv4 protocols in user space
  Control, speed, troubleshooting
Allow us to implement new IPv4 protocols
Allows us to control the IP header
  Control option fields (beyond setsockopt() )
  Test / control packet fragmentation

## Slide 3: Limitations?
Reliability Loss
No Ports
Nonstandard communication
No Automatic ICMP
Raw TCP / UDP unlikely
Requires root / admin

## Slide 4: OS Involvement in Sockets
User Space
Kernel Space
Socket App
TCP/IP Stack
Linux
Socket ( AF_INET,
SOCK_STREAM,
IPPROTO_TCP)
Socket ( AF_INET,
SOCK_RAW,
IPPROTO_ICMP)
Socket ( AF_PACKET,
SOCK_RAW,
htons(ETH_P_IP))
Identify
Socket Type
Identify
Socket Type
Identify
Socket Type
TCP
IP
Ethernet

## Slide 5: Normal Socket Operation (TCP)
Create a socket
  s = socket (PF_INET, SOCK_STREAM, IPPROTO_TCP)
Bind to a port (optional)
  Identify local IP and port desired and create data structure
  bind (s, (struct sockaddr *) &sin, sizeof(sin))
Establish a connection to server
  Identify server IP and port
  connect (s, (struct sockaddr *) &sin, sizeof(sin))
Send / Receive data
  Place data to be send into buffer
  recv (s, buf, strlen(buf), 0);

## Slide 6: Normal Socket Operation (TCP)
User Space
Kernel Space
Socket App
Protocol
Linux
socket ( )
Create socket
TCP, IP, Internet
connect( )
Bind to local port:
Connect to remote port
send( )
TCP, IP, Internet
Pass data thru local
stack to remote port
OK
OK
OK
TCP

## Slide 7: Raw Sockets Operation (ICMP)
Create a socket
  s = socket (PF_INET, SOCK_RAW, IPPROTO_ICMP)
Since there is no port, there is no bind *
There is no TCP, so no connection *
Send / Receive data
  Place data to be sent into buffer
  sendto (s, buf, strlen(buf), 0, addr, &len);
* More later

## Slide 8: Raw Sockets Operation (ICMP)
User Space
Kernel Space
Socket App
Protocol
Linux
socket ( )
Create socket
sendto( )
IP, Internet
Pass data thru local
stack to remote host
OK
OK
ICMP

## Slide 9: Create a Raw Socket
s = socket (AF_INET, SOCK_RAW, protocol)
  IPPROTO_ICMP, IPPROTO_IP, etc.
Can create our own IP header if we wish
  const int on = 1;
  setsockopt (s, IPPROTO_IP, IP_HDRINCL, &on, sizeof (on));
Can “bind”
  Since we have no port, the only effect is to associate a local IP address with the raw socket. (useful if there are multiple local IP addrs and we want to use only 1).
Can “connect”
  Again, since we have no TCP, we have no connection. The only effect is to associate a remote IP address with this socket.

## Slide 10: Raw Socket Output
Normal output performed using sendto or sendmsg.
  Write or send can be used if the socket has been connected
If IP_HDRINCL not set, starting addr of the data (buf) specifies the first byte following the IP header that the kernel will build.
  Size only includes the data above the IP header.
If IP_HDRINCL is set, the starting addr of the data identifies the first byte of the IP header.
  Size includes the IP header
  Set IP id field to 0 (tells kernel to set this field)
  Kernel will calculate IP checksum
Kernel can fragment raw packets exceeding outgoing MTU

## Slide 11: Raw Socket Input
Received TCP / UDP NEVER passed to a raw socket.
Most ICMP packets are passed to a raw socket
  (Some exceptions for Berkeley-derived implementations)
All IGMP packets are passed to a raw socket
All IP datagrams with a protocol field that the kernel does not understand (process) are passed to a raw socket.
If packet has been fragmented, packet is reassembled before being passed to raw socket

## Slide 12: Conditions that include / exclude passing to specific raw sockets
If a nonzero protocol is specified when raw socket is created, datagram protocol must match
If raw socket is bound to a specific local IP, then destination IP must match
If raw socket is “connected” to a foreign IP address, then the source IP address must match

## Slide 13: Ping – Overview
This example modified from code by Walton (Ch 18)
Very simple program that uses ICMP to send a ping to another machine over the Internet.
Provides the option to send a defined number of packets (or will send a default 25).
We will build an ICMP packet (with a proper header, including checksum) that will be updated each time we send a new packet.
We will display the raw packet that is received back from our destination host and will interpret some of the data.
  (Output format is different from standard ping)

## Slide 14: ICMP Packet header
struct icmphdr {
u_int8_t type // ICMP message type (0)
u_int8_t code // ICMP type sub-code (0)
u_int16_t checksum E306, etc.
u_int16_t id // echo datagram id (use pid)
u_int16_t sequence // echo seq # 1, 2, 3, etc.
};
Packet body:
0 1 2 3 4 5 6 7 8 9 : ; < = > ? … B

## Slide 15: myNuPing.c (overview)
Global Declarations
  Struct packet { }, some variables
unsigned short checksum (void *b, int len)
  Calculate checksum for ICMP packet (header and data)
void display (void *buf, int bytes)
  Format a received packet for display.
void listener (void)
  Separate process to capture responses to pings
void ping (struct sockaddr_in *addr)
  Create socket and send out pings 1/sec to specified IP addr
int main (int count, shar *strings[ ])
  Test for valid instantiation, create addr structure
  Fork a separate process (listener) and use existing process for ping

## Slide 16: #defines and checksum calc
#define PACKETSIZE 64
struct packet {
struct icmphdr hdr;
char msg[PACKETSIZE-sizeof(struct icmphdr)];
};
int pid=-1;
int loops = 25;
struct protoent *proto=NULL;
unsigned short checksum(void *b, int len) {
unsigned short *buf = b;
unsigned int sum=0;
unsigned short result;
for ( sum = 0; len > 1; len -= 2 )
sum += *buf++;
if ( len == 1 )
sum += *(unsigned char*)buf;
sum = (sum >> 16) + (sum & 0xFFFF);
sum += (sum >> 16);
result = ~sum;
return result;
}

## Slide 17: display - present echo info
void display(void *buf, int bytes) {
int i;
struct iphdr *ip = buf;
struct icmphdr *icmp = buf+ip->ihl*4;
printf("----------------\n");
for ( i = 0; i < bytes; i++ ) {
if ( !(i & 15) ) printf("\n%04X: ", i);
printf("%02X ", ((unsigned char*)buf)[i]);
}
printf("\n");
printf("IPv%d: hdr-size=%d pkt-size=%d protocol=%d TTL=%d src=%s ",
ip->version, ip->ihl*4, ntohs(ip->tot_len), ip->protocol,
ip->ttl, inet_ntoa(ip->saddr));
printf("dst=%s\n", inet_ntoa(ip->daddr));
if ( icmp->un.echo.id == pid ) {
printf("ICMP: type[%d/%d] checksum[%d] id[%d] seq[%d]\n",
icmp->type, icmp->code, ntohs(icmp->checksum),
icmp->un.echo.id, icmp->un.echo.sequence);
}
}

## Slide 18: Listener - separate process to listen for and collect messages-
void listener(void) {
int sd, i;
struct sockaddr_in addr;
unsigned char buf[1024];
sd = socket(PF_INET, SOCK_RAW, proto->p_proto);
if ( sd < 0 ) {
perror("socket");
exit(0);
}
for (i = 0; i < loops; i++) {
int bytes, len=sizeof(addr);
bzero(buf, sizeof(buf));
bytes = recvfrom(sd, buf, sizeof(buf), 0, (struct sockaddr *) &addr, &len);
if ( bytes > 0 )
display(buf, bytes);
else
perror("recvfrom");
}
exit(0);
}

## Slide 19: ping - Create message and send it
void ping(struct sockaddr_in *addr)
{
const int val=255;
int i, j, sd, cnt=1;
struct packet pckt;
struct sockaddr_in r_addr;
sd = socket(PF_INET, SOCK_RAW, proto->p_proto);
if ( sd < 0 )
{
perror("socket");
return;
}
if ( setsockopt(sd, SOL_IP, IP_TTL, &val, sizeof(val)) != 0)
perror("Set TTL option");
if ( fcntl(sd, F_SETFL, O_NONBLOCK) != 0 )
perror("Request nonblocking I/O");

## Slide 20: ping (cont)
for (j = 0; j < loops; j++) { // send pings 1 per second
int len=sizeof(r_addr);
printf("Msg #%d\n", cnt);
if ( recvfrom(sd, &pckt, sizeof(pckt), 0, (struct sockaddr *)&r_addr, &len) > 0 )
printf("***Got message!***\n");
bzero(&pckt, sizeof(pckt));
pckt.hdr.type = ICMP_ECHO;
pckt.hdr.un.echo.id = pid;
for ( i = 0; i < sizeof(pckt.msg)-1; i++ )
pckt.msg[i] = i+'0';
pckt.msg[i] = 0;
pckt.hdr.un.echo.sequence = cnt++;
pckt.hdr.checksum = checksum(&pckt, sizeof(pckt));
if (sendto(sd, &pckt, sizeof(pckt), 0, (struct sockaddr *) addr, sizeof(*addr)) <= 0)
perror("sendto");
sleep(1);
}
}

## Slide 21: myNuPing.c – main()
int main(int count, char *argv[]) {
struct hostent *hname;
struct sockaddr_in addr;
loops = 0;
if ( count != 3 ) {
printf("usage: %s <addr> <loops> \n", argv[0]);
exit(0);
}
if (count == 3) // WE HAVE SPECIFIED A MESSAGE COUNT
loops = atoi(argv[2]);
if ( count > 1 ) {
pid = getpid();
proto = getprotobyname("ICMP");
hname = gethostbyname(argv[1]);
bzero(&addr, sizeof(addr));
addr.sin_family = hname->h_addrtype;
addr.sin_port = 0;
addr.sin_addr.s_addr = *(long*)hname->h_addr;
if ( fork() == 0 )
listener();
else
ping(&addr);
wait(0);
}
else
printf("usage: myping <hostname>\n");
return 0;
}

## Slide 22: “Ping” Output
[root]# ./myNuPing 134.193.12.34 2
Msg #1
----------------
0000: 45 00 00 54 CC 38 40 00 80 01 1F BE 86 12 34 56
0010: 86 12 34 57 00 00 E4 06 DF 07 01 00 30 31 32 33
0020: 34 35 36 37 38 39 3A 3B 3C 3D 3E 3F 40 41 42 43
0030: 44 45 46 47 48 49 4A 4B 4C 4D 4E 4F 50 51 52 53
0040: 54 55 56 57 58 59 5A 5B 5C 5D 5E 5F 60 61 62 63
0050: 64 65 66 00
IPv4: hdr-size=20 pkt-size=84 protocol=1 TTL=128 src=134.193.12.35 dst=134.193.12.34
ICMP: type[0/0] checksum[58374] id[2015] seq[1]
Msg #2
***Got message!***
----------------
0000: 45 00 00 54 CC 39 40 00 80 01 1F BD 86 12 34 56
0010: 86 12 34 57 00 00 E3 06 DF 07 02 00 30 31 32 33
0020: 34 35 36 37 38 39 3A 3B 3C 3D 3E 3F 40 41 42 43
0030: 44 45 46 47 48 49 4A 4B 4C 4D 4E 4F 50 51 52 53
0040: 54 55 56 57 58 59 5A 5B 5C 5D 5E 5F 60 61 62 63
0050: 64 65 66 00
IPv4: hdr-size=20 pkt-size=84 protocol=1 TTL=128 src=134.193.12.35 dst=134.193.12.34
ICMP: type[0/0] checksum[58118] id[2015] seq[2]
[root]#

## Slide 23: Summary
Raw Sockets allow access to Protocols other than the standard TCP and UDP
Performance and capabilities may be OS dependent.
  Some OSs block the ability to send packets that originate from raw sockets (although reception may be permitted).
Raw sockets remove the burden of the complex TCP/IP protocol stack, but they also remove the safeguards and support that those protocols provide